## Slide 1: RT-1 (robot transformer)

## Slide 2: content
1. task
2. dataset
3. Preliminaries
4. model architecture

## Slide 3: Task define
building and demonstrating a general robot learning system that can absorb large amounts of data and generalize effectively by using Transformer architecture
7 DOF (x, y, z, roll, pitch, yaw, grip)
three of environment (kitchens)

## Slide 4: Dataset composition
Some simple instructions
Two type of split pivot ( skill, object )
Ex) pick up coke can, throw apple

## Slide 5: Preliminaries
aim to learn robot policies to solve language-conditioned tasks from vision.
RT-1 uses a Transformer to parameterize the policy π.
dataset D = {(i(n), {(x(n)_t , a(n)_t )}T(n)_t=0 )}N_n=0 of episodes

## Slide 6: Model

## Slide 7: Instruction and image tokenization
Input : 6 image (300 x 300), instruction
Image  EfficientNetB3  feature map (9 x 9 x 512)
Instruction  Sentence Encoder  FiLM

## Slide 8: TokenLearner
Large number of tokens  smaller number of tokens
81 (9 x 9) tokens  8 tokens
6 image per 8 tokens  total 48 tokens

## Slide 9: Transformer
decoder-only sequence model with 8 self-attention layers

## Slide 10: Action tokenization
Total 11 variables
1 : mode (controlling arm, base
or terminating the episode )
7 : arm movement ( x, y, z, roll, pitch, yaw, grib)
3 : base movement ( x, y, yaw )
All of variables are represented by 256 bins

## Slide 11: Appendix
Loss function : CE
Inference speed : consistently speed ( control frequency 3Hz, latency 100ms )
Good performance about incorporating simulation data
It can absorb data from different robots.